## Slide 2: Limitations of single-modal data perception
Camera
  Mainly captured in the lower position of the front view
  Objects may be occluded in more complex scenes
Lidar
  Various resolutions at different distances
  Vulnerable to extreme weather

## Slide 3: Contributions
A new taxonomy defined by the feature representation
  Strong-fusion
    Early-fusion, deep-fusion, late-fusion, asymmetry-fusion
  Weak-fusion
An in-depth survey about the data format and representation of the LiDAR and camera branch and a discussion about their different characteristics
A detailed analysis about the remaining problems and an introduction to several potential research directions

## Slide 4: Multi-modal Sensor Fusion Perception Tasks
Object Detection
Semantic Segmentation
Others
  Object classification
  Depth completion and prediction

## Slide 5: Open competitions and Datasets
KITTI
  2D, 3D, BEV
  Cars, pedestrians, cyclists
  Easy, medium, hard
Waymo
  20s / scene
  Vehicles, cyclists, pedestrians
nuScenes
  23 categories

## Slide 6: Open competitions and Datasets

## Slide 7: Representations for LiDAR
Point-based
  Redundancy, slow
Voxel-based
  Centroid, local density, local offset, local linearity, local curvature, …
  Reduced redundancy, faster
2D-mapping-based
  Camera plane map (CPM)
  Bird’s eye view (BEV)

## Slide 8: Fusion Methodology

## Slide 9: Strong Fusion

## Slide 10: Early-fusion
LiDAR: 3D points with reflectance, voxelized tensor, front-view / range-view / bird’s eye view, pseudo-point clouds
Camera: data-level or feature-level

## Slide 11: Deep-fusion
LiDAR: feature-level
Camera: data-level or feature-level
Can be done in a cascading way, which both leverage raw and high-level semantic information

## Slide 12: Late-fusion
Fuse the result of pipelines in each modality
Can be regarded as a kind of ensemble method that utilizes multi-modal information to optimize the final proposal

## Slide 13: Asymmetry-fusion
Has at least one branch dominating while other branches provide auxiliary information to conduct the final task
Only have proposals from one branch

## Slide 14: Weak Fusion
Use rule-based methods to utilize data in one modality as a supervision signal to guide the interaction of another modality

## Slide 15: Opportunities in Multi-Modal Fusion
More Advanced Fusion Methodology
  Misalignment and Information Loss
    Inaccurate intrinsic and extrinsic, sensory noise
    Information loss in transformation
  More Reasonable Fusion Operations
    Currently: concatenation, element-wise multiplication
Multi-Source Information Leverage
  With More Potential Useful Information
    Lack the effective use of temporal, contextual, and spatial information
  Self-Supervision for Representation Learning
    Use the multi-modal data for self-supervised learning

## Slide 16: Opportunities in Multi-Modal Fusion (Cont.)
Intrinsic Problems in Perception Sensors
  Data Domain Bias
    Sensor, weather, season, location
  Conflicts with Data Resolution
    The spatial density of LiDAR is notably lower than that of the image